## Slide 1: Attack Traceback
Kai Bu
kaibu@zju.edu.cn
http://list.zju.edu.cn/kaibu/netsec2022
08

## Slide 2: Attack Detected!

## Slide 3: Attack From Where?

## Slide 4: Attack From Where?
does source IP address say it all?

## Slide 5: Attack From Where?
remember IP spoofing?

## Slide 6: Attack From Where?
remember IP spoofing?
does ingress filtering filter them all?

## Slide 7: Ingress Filtering
How to find packet origin?
Ingress filtering policy:
ISP only forwards packets with legitimate source IP
ISP
Internet
Notes: Packet enter internet via ISP

## Slide 8: Ingress Filtering
Implementation challenges:
All ISPs need to do this — requires global coordination:
If 10% of networks don’t implement, there’s no defense;
No incentive for an ISP to implement — doesn’t affect them;
Ingress filtering policy:
ISP only forwards packets with legitimate source IP
Notes: Packet enter internet via ISP

## Slide 9: Ingress Filtering
Implementation challenges:
As of 2017 (from CAIDA):
33% of autonomous systems allow spoofing;
23% of announced IP address space allow spoofing;
Ingress filtering policy:
ISP only forwards packets with legitimate source IP
Notes: Packet enter internet via ISP

## Slide 10
To remember where you come from
Let Transit Routers Help!
is part of where you’re going.
~ Anthony Burgess

## Slide 11: IP Traceback
Goal
given set of attack packets
determine path to source
How
change routers to record info in packets

## Slide 12: IP Traceback
Goal
given set of attack packets
determine path to source
How
change routers to record info in packets
Assumptions
trusted routers
sufficient packets to track
stable route from attacker to victim

## Slide 13: IP Traceback
Write path into packets
router adds its own IP address to packet
victim reads path from packet
Deterministic Packet Marking

## Slide 14: IP Traceback
Write path into packets
router adds its own IP address to packet
victim reads path from packet
Limitations
requires space in packet
path can be long
no extra fields in current IP format (changes to packet format too much to expect)

## Slide 15: IP Traceback
Sample and Merge
store one link in each
packet;
router probabilistically
stores own address;
fixed space regardless of
path length;
Probabilistic Packet Marking
R6
R7
R8
A4
A5
A1
A2
A3
R9
R10
R12
V

## Slide 16: IP Traceback
Edge Sampling: fields into packet
edge: start and end IP addresses
distance: no. of hops since edge stored
Marking procedure of router R

## Slide 17: IP Traceback
Packet received
R1 receives packet from source or another router;
packet contains space for start, end, distance;
R1
R2
R3
packet
s
e
d

## Slide 18: IP Traceback
Begin writing edge
R1 chooses to write start of edge;
sets distance to 0;
R1
R2
R3
packet
R1
0

## Slide 19: IP Traceback
Finish writing edge
R2 chooses not to overwrite edge;
distance is 0: write end of edge, increment distance to 1;
packet
R1
R2
1
R1
R2
R3

## Slide 20: IP Traceback
Increment distance
R3 chooses not to overwrite edge;
distance>0: increment distance to 2;
packet
R1
R2
2
R1
R2
R3

## Slide 21: IP Traceback
Increment distance
R3 chooses not to overwrite edge;
distance>0: increment distance to 2;
packet
R1
R2
2
R1
R2
R3
What if traceback fields are tampered with…

## Slide 22: ICMP Traceback
iTrace
Each router samples one of packets it is forwarding and copies the contents and adjacent routers’ info into an ICMP traceback message
Router uses HMAC and X.509 digital certificate for authenticating traceback messages
Router sends ICMP traceback messages to the destination

## Slide 23: ICMP Traceback
iTrace
Each router samples one of packets it is forwarding and copies the contents and adjacent routers’ info into an ICMP traceback message
Router uses HMAC and X.509 digital certificate for authenticating traceback messages
Router sends ICMP traceback messages to the destination

## Slide 24: ICMP Traceback
iTrace
Require all the routers transmitting attack traffic be enabled with iTrace to construct an entire attack path
yet ICMP packets are usually filtered… because of ICMP Ping Flood Attack…

## Slide 25: ICMP Traceback
iTrace
Require all the routers transmitting attack traffic be enabled with iTrace to construct an entire attack path
yet ICMP packets are usually filtered… because of ICMP Ping Flood Attack…
yet not all packets are sampled on every hop

## Slide 26: Path Validation
PoC: Proof of Consent
certify the provider’s consent to carry traffic along the path
PoP: Proof of Provenance
allow upstream nodes to prove to downstream nodes that they carried the packet

## Slide 27: Path Validation

## Slide 28: Path Validation
https://cs.nyu.edu/~mwalfish/papers/icing-conext11.pdf

## Slide 29
should every packet be always marked?
how frequent is attack?

## Slide 30
should some packet be always sampled?
how frequent is attack?

## Slide 31
only when needed
Let Transit Routers Help!

## Slide 32: Link Testing
Traceback from the router closest to the victim
Determine the upstream link that is used to carry out the attack traffic
Recursively apply the previous technique until the attack source is reached
https://books.google.ca/books?id=cxdNEAAAQBAJ
Notes: https://books.google.ca/books?id=cxdNEAAAQBAJ&pg=PA121

## Slide 33: Link Testing
Traceback from the router closest to the victim
Determine the upstream link that is used to carry out the attack traffic
Recursively apply the previous technique until the attack source is reached
Has to take effect while the attack is in progress
Notes: https://books.google.ca/books?id=cxdNEAAAQBAJ&pg=PA121

## Slide 34: Link Testing
Traceback from the router closest to the victim
Determine the upstream link that is used to carry out the attack traffic
Recursively apply the previous technique until the attack source is reached
Input Debugging
Controlled Flooding
Notes: https://books.google.ca/books?id=cxdNEAAAQBAJ&pg=PA121

## Slide 35: Input Debugging
Find attack signature, the common feature contained in all attack packets
Communicate the attack signature to the upstream router, which then filters attack packets and determines the port of entry
Recursively apply the previous technique on the upstream routers until reaching the attack source

## Slide 36: Input Debugging
Find attack signature, the common feature contained in all attack packets
Communicate the attack signature to the upstream router, which then filters attack packets and determines the port of entry
A considerable management overhead at the ISP level to communicate and coordinate the traceback

## Slide 37: Controlled Flooding
Need collaborative hosts
Force the hosts to flood the links to upstream routers
Since buffer on victim is shared by all incoming links, flooding the link carrying out attack leads to drops of attack packets
Recursively apply the previous technique on the upstream routers until reaching the attack source

## Slide 38: Controlled Flooding
Need collaborative hosts
Force the hosts to flood the links to upstream routers
Since buffer on victim is shared by all incoming links, flooding the link carrying out attack leads to drops of attack packets
Require an accurate topology map High overhead given multiple attacking sources (e.g., DDoS)

## Slide 39
link testing requires ongoing attack…
post-attack traceback?

## Slide 40
log packets on routers to support query
Let Transit Routers Help!

## Slide 41: Logging-Based Traceback
Routers store packet logs
Victim queries the closest routers about packet appearance of attack packets
The router containing attack packets recursively query upstream routers until reaching the attack source

## Slide 42: Logging-Based Traceback
see packet P?
see packet P?
yes

## Slide 43: Logging-Based Traceback
see packet P?
see packet P?
yes
what packet data to log?

## Slide 44: Logging-Based Traceback
Raw packets? high storage overhead on routers
Hash of invariant content per packet? still high storage overhead given high traffic rate

## Slide 45: Logging-Based Traceback
Raw packets? high storage overhead on routers
Hash of invariant content per packet? still high storage overhead given high traffic rate
How to efficient memership query?

## Slide 46: Bloom Filter
Effeficent set memership query using multiple hashes per set elements
Use a bitmap, a bit of which is set of one element is hashed to this position

## Slide 47: Bloom Filter
Is Cathy an allowed user?

## Slide 48: Bloom Filter
Is Jonas an allowed user?

## Slide 49: Bloom Filter
Is John an allowed user?

## Slide 50: Bloom Filter
Is Cathy an allowed user?
No False Negative:
For users not in,
not all hashed positions are set.

## Slide 51: Bloom Filter
Is Jonas/John an allowed user?
Yet False Positive:
For users with all
hashed positions being set,
users are not necessarily in.
Notes: The equation is not as complicated as it may appear: (1 - 1/m)^{kn} is the probability that any bit is not set, given n elements that each hashes k times to any of m bit positions. Finally, to get a false positive, all of the k bit positions hashed onto by the ID that causes a false positive must be set.

## Slide 52: Bloom Filter
Is Jonas/John an allowed user?
Yet False Positive:
m-size bitmap,
n members,
k hash functions:
Notes: The equation is not as complicated as it may appear: (1 - 1/m)^{kn} is the probability that any bit is not set, given n elements that each hashes k times to any of m bit positions. Finally, to get a false positive, all of the k bit positions hashed onto by the ID that causes a false positive must be set.

## Slide 53: Bloom Filter
Hash invariant content of packets
Total Length
Identification
Checksum
Ver
TOS
HLen
TTL
Protocol
Source Address
Destination Address
Fragment Offset
M
F
D
F
Options
Remainder of Payload
First 8 bytes of Payload
28
bytes

## Slide 54
SPIE System:
Source Path Isolation Engine

## Slide 55: Performance Comparison
https://dl.acm.org/doi/10.1145/347057.347560

## Slide 56: ?

## Slide 57
were routing protocols modified…

## Slide 58: Readings
Practical Network Support for IP Traceback
by Stefan Savage et al.
Network Security Know It All
by James Joshi

## Slide 59
Thank You
be on the road
Notes: Run your own race.